## Slide 1: Pi Pico OOP Mini Project
Ben Jones
Tempe High School
Lecture 4

## Slide 2: Simple Open Loop Control System
Traffic Lights remain green until pressed (idle state).
Button pressed triggers state change.
Lights rotate through a pattern based on time.
System returns to idle state

## Slide 3: Today
Implement a basic button class
Create an interrupt and debounce the button
Unit test the pedestrian button

## Slide 4: Create new files
v05.py in project\py_scripts\
pedestrian_button.py in project\lib\

## Slide 5: Pedestrian_Button Imports
from machine import Pin
import time

## Slide 6: Pedestrian_Button Class Attributes
class Pedestrian_Button(Pin):
# child class inherits the parent 'Pin' class
  def __init__(self, pin, debug):
    super().__init__(pin, Pin.IN, Pin.PULL_DOWN)
    self.__debug = debug
    self.__pin = pin
    self.__last_pressed = 0 # Track the last time the button was pressed
    self.__pedestrian_waiting = False
    self.button_state

## Slide 7: Pedestrian_Button “Getter”
@property
def button_state(self):
  if self.__debug:
    print(f"Button connected to Pin {self.__pin} is {'WAITING' if self.__pedestrian_waiting else 'NOT WAITING'}")
  return self.__pedestrian_waiting

## Slide 8: Pedestrian_Button “Setter”
@button_state.setter
def button_state(self, value):
  self.__pedestrian_waiting = value
  if self.__debug:
    print(f"Button state on Pin {self.__pin} set to {value}")

## Slide 9: Pedestrian_Button Interrupt
class Pedestrian_Button(Pin):
# child class inherits the parent 'Pin' class
  def __init__(self, pin, debug):
    …
    # Set up interrupt on rising edge
    self.irq(trigger=Pin.IRQ_RISING, handler=self.callback)

## Slide 10: Pedestrian_Button Interrupt Callback Method
def callback(self, pin):
  current_time = time.ticks_ms() # Get the current time in milliseconds
  if (time.ticks_diff(current_time, self.__last_pressed) > 200): # 200ms debounce delay
    self.__last_pressed = current_time
    self.__pedestrian_waiting = True
    if self.__debug:
      print(f"Button pressed on Pin {self.__pin} at {current_time}ms")

## Slide 11: Unit Test the Pedestrian_Button class
Your unit test should test all methods, where possible, because it involves a physical button you should design a manual test.
Pause the video, design your unit test, then check your unit tests against my suggested batch of unit tests.