## Slide 1: Pi Pico OOP Mini Project
Ben Jones
Tempe High School
Lecture 3

## Slide 2: Simple Open Loop Control System
Traffic Lights remain green until pressed (idle state).
Button pressed triggers state change.
Lights rotate through a pattern based on time.
System returns to idle state

## Slide 3: Today
Multiple Inheritance
Association
Setup controller states

## Slide 4: Create new files
v07.py in project\py_scripts\
controller.py in project\lib\

## Slide 5: Multiple Inheritance
Multiple Inheritance is used to inherit the properties of multiple classes. However, Python does not allow multiple inheritance from classes that have incompatible memory layouts at the C level, which is common with hardware classes in MicroPython.
https://github.com/TempeHS/MicroPython_OOP_Pi_Pico_Mini_Project_Source/blob/main/tutorials/Lecture5.md#multiple-inheritance

## Slide 6: Association
Association in Object-Oriented Programming (OOP) describes the relationship between two separate classes that are connected, but neither “inherits" the other. It simply means that objects of one class interact with or use objects of another class.
Run: v15.py

## Slide 7: Setup Controller States
In the context of a microcontroller, state refers to the current values or conditions of the system’s internal variables, inputs, outputs, and memory at a specific moment in time. State is crucial for determining how the microcontroller should behave next.
For example, in a simple traffic light controller, one of the states could be “Traffic_Go” in which the green lights are on() while both the red and amber lights are off().

## Slide 8: Describe the states
Think about this system and describe the states and to triggers for each statte

## Slide 9: States
State | Trigger | Light Pattern
Idle | Button Press | 
Changing |  | 
Walk |  | 
Walk stop warning |  | 

## Slide 10: States
 | Change Trigger | Light Pattern
Idle | Button Press | Ped Red On Car Green On Rest Off
Changing | Time | Ped Red On Car Amber On Rest Off
Walk | Time | Ped Green On Car Red On Audio Warning Rest Off
Walk stop warning | Timer | Ped Red Flashing Car Red On Rest Off

## Slide 11: Pedestrian_Button Imports
from led_light import Led_Light
from pedestrian_button import Pedestrian_Button
from audio_notification import Audio_Notification
from time import sleep, time

## Slide 12: Pedestrian_Button Class Attributes
class Controller:
  def __init__(
  self, ped_red, ped_green, car_red, car_amber, car_green, button, buzzer, debug):
    self.__Ped_Red = ped_red
    self.__Ped_Green = ped_green
    self.__Car_Red = car_red
    self.__Car_Amber = car_amber
    self.__Car_Green = car_green
    self.__Buzzer = buzzer
    self.__Button = button
    self.__debug = debug

## Slide 13: Create a method for each state
def idle(self):
def change(self):
def walk(self):
def walk_warning(self):
Pause the video, design your states, then check your states against my suggested states.