## Slide 1: Pi Pico OOP Mini Project
Ben Jones
Tempe High School
Lecture 4

## Slide 2: Simple Open Loop Control System
Traffic Lights remain green until pressed (idle state).
Button pressed triggers state change.
Lights rotate through a pattern based on time.
System returns to idle state

## Slide 3: Today
Implement an audio notification class
Implement a non-blocking beep
Unit test the audio notification

## Slide 4: Create new files
v06.py in project\py_scripts\
audio_notification.py in project\lib\

## Slide 5: Audio_Notification Imports
from machine import Pin, PWM
from time import sleep, time

## Slide 6: Audio_Notification Class Attributes
class Audio_Notification(PWM):
  def __init__(self, pin, debug=False):
    super().__init__(Pin(pin))
    self.__debug = debug
    self.duty_u16(0) # Start with buzzer off
    self._last_toggle_time = time()

## Slide 7: Audio_Notification .beep() Method
def beep(self, freq=1000, duration=500):
  if self.__debug:
    print("Beep")
  self.freq(freq)
  self.duty_u16(32768) # 50% duty cycle
  sleep(duration / 1000)
  self.duty_u16(0) # Turn off after beep

## Slide 8: Audio_Notification .warning_on() Method
def warning_on(self):
  if self.__debug:
    print("Warning on")
  now = time()
  if now - self._last_toggle_time >= 0.5:
    self.beep(freq=500, duration=100)
    self._last_toggle_time = now

## Slide 9: Audio_Notification .warning_off() Method
def warning_off(self):
  if self.__debug:
    print("Warning off")
  self.duty_u16(0) # Turn off sound

## Slide 10: Unit Test the Audio_Notification class
Your unit test should test all methods, where possible, because it involves an auditory sound you should design a manual test.
Pause the video, design your unit test, then check your unit tests against my suggested batch of unit tests.